## Slide 1
XAY DUNG GIAI PHAP TRUYEN TIN BAO MAT GIUA CAC THIET BI IoT
DE TAI: Xay dung giai phap truyen tin bao mat giua cac thiet bi IoT
Sinh vien: Do Anh Quan & Ta Huy Hoang
Huong dan: Thay Haihd
2026

## Slide 2
NOI DUNG TRINH BAY
Chuong 1: Gioi thieu de tai
Chuong 2: Nhung co so ly thuyet
Chuong 3: Phan tich va thiet ke he thong
Chuong 4: Xay dung va thuc nghiem he thong
Xay dung giai phap truyen tin bao mat giua cac thiet bi IoT

## Slide 3
3.1 Phan tich bai toan
Mo hinh he thong: Node Xi --> Gateway Y --> Flask Server --> SQLite --> Dashboard
Yeu cau | Mo ta
R1 | Thiet bi IoT gui du lieu cam bien qua LoRa
R2 | Gateway phat hien node qua Beacon, thuc hien bat tay Req/Ack
R3 | Du lieu duoc ma hoa (AES-128-CBC) tu thiet bi den Server
R4 | Server xu ly, hien thi tren Web Map voi Dashboard
Xay dung giai phap truyen tin bao mat giua cac thiet bi IoT

## Slide 4
3.2 Kien truc he thong 5 lop
Lop | Thanh phan | Chuc nang
Sensor Layer | Node Xi (ESP32) | Tao du lieu, ma hoa AES-128-CBC
Gateway Layer | Gateway Y | Lau du lieu, chuyen tiep, KHONG giai ma
Server Layer | Flask Server | Giai ma duy nhat, kiem tra seq, benchmark
Storage Layer | SQLite DB | Luu tru devices, telemetry, benchmark
Display Layer | Streamlit Dashboard | Bieu do, ban do, thong ke
Xay dung giai phap truyen tin bao mat giua cac thiet bi IoT

## Slide 5
3.2.2 Chuc nang Node Xi (14 chuc nang)
STT | Chuc nang
1 | Khoi tao thiet bi
2 | Tao Beacon
3 | Gui Beacon
4 | Cho ACK
5 | Kiem tra ACK
6 | Tao du lieu cam bien
7 | Tao du lieu GPS
STT | Chuc nang
8 | Tao JSON
9 | Them sequence number
10 | Tao IV
11 | Ma hoa AES-128-CBC
12 | Tao hex payload
13 | Gui payload
14 | Cap nhat seq / chong replay
Xay dung giai phap truyen tin bao mat giua cac thiet bi IoT

## Slide 6
3.3.3 Cau truc goi tin
Loai | Dang | Vi du
Beacon | B¦<Xi_ID> | B¦Xi_01
ACK | A¦<Xi_ID>¦<Y_ID> | A¦Xi_01¦Y_01
Data | D¦<Xi_ID>¦<hex> | D¦Xi_01¦8c94a1...
Cau truc JSON (13 truong):
{ "id", "t", "h", "p", "co2", "co", "nh3", "lat", "lon", "alt", "sats", "gw", "seq" } Payload: IV (16B) + Ciphertext -> hex (~416 ky tu)
Xay dung giai phap truyen tin bao mat giua cac thiet bi IoT

## Slide 7
3.4 Thiet ke IoT Gateway
Thiet ke quan trong: Gateway KHONG giai ma du lieu
5 chuc nang chinh:
1. Nhan Beacon tu Xi
2. Tao va gui ACK
3. Nhan payload ma hoa
4. Chuyen tiep len Server (HTTP POST)
5. Nhan phan hoi, hien thi trang thai
Loi ich:
- Gateway don gian, giam do phuc tap
- Neu Gateway bi truy cap, du lieu van an toan
- Gateway chi chuyen tiep, khong phan tich noi dung
Xay dung giai phap truyen tin bao mat giua cac thiet bi IoT

## Slide 8
3.5 Thiet ke Flask Server
Endpoint: POST /receive-data
10 dieu kien xac thuc:
1. Request co JSON body
2. Body co truong 'payload'
3. Payload la hex hop le
4. Payload du dai (>= 32 byte)
5. Giai ma thanh cong
6. Plaintext la JSON hop le
7. JSON co device_id
8. JSON co sequence number
9. Seq moi hon last_seq
10. Ghi vao database thanh cong
11 truong hop loi:
- Missing body/payload
- Invalid hex, too short
- Wrong AES key
- Invalid padding
- Invalid JSON
- Missing id/seq
- Old sequence (replay!)
- Device not found
- Database error
Xay dung giai phap truyen tin bao mat giua cac thiet bi IoT

## Slide 9
3.6 Co che ma hoa AES-128-CBC
Luong ma hoa:
Du lieu cam bien --> JSON --> Them id/gw/seq --> JSON bytes --> Padding --> IV 16B --> AES-128-CBC --> IV+Ciphertext --> Hex --> Gui
Luong giai ma:
Hex payload --> Bytes --> Cat IV (16B) + Ciphertext --> AES-128-CBC decrypt --> Xoa padding --> JSON --> Xac thuc
Thanh phan | Kich thuoc | Ghi chu | 
Plaintext JSON | ~180 bytes | 13 truong cam bien | 
Key: Pre-Shared Key 16 byte (chi o Xi va Server, KHONG o Gateway)
Xay dung giai phap truyen tin bao mat giua cac thiet bi IoT

## Slide 10
3.7 Luu do hoat dong
Hinh 3.12 - Luong binh thuong:
Xi gui Beacon --> Gateway ACK --> Xi ma hoa & gui --> Server giai ma, kiem tra seq, luu DB --> HTTP 200
Hinh 3.13 - Phat hien replay:
Gateway chuyen tiep --> Server giai ma OK --> Nhung seq <= last_seq --> HTTP 403
Hinh 3.14 - Giai ma that bai:
Gateway chuyen tiep --> Server giai ma that bai --> Phan hoi loi
Xay dung giai phap truyen tin bao mat giua cac thiet bi IoT

## Slide 11
CHUONG 4: XAY DUNG VA THUC NGHIEM HE THONG
4.1 Moi truong phat trien
4.2 Cau truc ma nguon
4.3 Xay dung Node Xi
4.4 Xay dung Gateway Y
4.5 Xay dung Flask Server
4.6 Xay dung co so du lieu
4.7 Xay dung Dashboard
4.8 Kich ban kiem thu
4.9 Ket qua kiem thu
4.10 Danh gia hieu nang
4.11 Kiem thu tan cong phat lai
4.12 Han che va huong phat trien
Xay dung giai phap truyen tin bao mat giua cac thiet bi IoT

## Slide 12
4.1 Moi truong phat trien
Thanh phan | Cong cu / Cong nghe
Microcontroller | ESP32 (Xtensa LX6 @ 240MHz, 520KB SRAM)
Board phan cung | TTGO T-Beam V08 (ESP32 + LoRa SX1276 + GPS)
Mo phong | Wokwi (ESP32 simulator)
Ngon ngu ESP32 | C/C++ (Arduino Framework)
Ma hoa | AES-128-CBC (mbedtls / PyCryptodome)
Backend | Python Flask 3.x
Database | SQLite 3
Dashboard | Streamlit + Folium + OpenStreetMap
Truyen tin | LoRa 433/868 MHz, Wi-Fi, HTTP/JSON
IDE | VS Code, Arduino IDE
Xay dung giai phap truyen tin bao mat giua cac thiet bi IoT

## Slide 13
4.2 Cau truc ma nguon du an
Thu muc | Noi dung
hardware/ | Firmware ESP32 (xi_node, y_gateway)
server/ | Flask server, dashboard, simulator, tests
wokwi/ | File mo phong Wokwi (2 node rieng)
docs/ | Tai lieu nghien cuu va hinh anh
.env | Biến moi truong (key, secret)
File | Chuc nang
app.py | Flask server chinh (177 dong)
init_db.py | Khoi tao SQLite database
dashboard.py | Streamlit Dashboard (4 tab)
simulator.py | Mo phong luong Xi->Y->Server
benchmark_crypto.py | Benchmark AES vs XOR
test_replay.py | Test chong replay (7 case)
test_replay_scenario.py | Test replay kich ban 4.16
Xay dung giai phap truyen tin bao mat giua cac thiet bi IoT

## Slide 14
4.3 Xay dung Node Xi
5 nhiem vu chinh: Beacon, cho ACK, doc cam bien, AES ma hoa, gui qua LoRa
Buoc | Mo ta
1. Beacon | Gui 'B¦Xi_01' qua LoRa (chu ky 3s)
2. Cho ACK | Cho 3s, parse 'A¦Xi_01¦Y_01'
3. Doc cam bien | BME280: nhiet do, do am, ap suat
4. Ma hoa | JSON (~180B) --> AES-128-CBC --> hex (~416 ky tu)
Ky thuat | Chi tiet
AES-128-CBC | mbedtls, HW accelerator: ~17-18us
Key | Pre-Shared 16 byte: key_x_1234567890
IV | 16 byte ngau nhien moi lan ma hoa
Seq | Random bat dau: 1000 + random(9000)
Xay dung giai phap truyen tin bao mat giua cac thiet bi IoT

## Slide 15
4.4-4.5 Xay dung Gateway va Server
Gateway Y:
- Scan Beacon --> gui ACK
- Nhan payload ma hoa --> chuyen tiep Server
- KHONG giai ma (bao mat)
- File: hardware/y_gateway/y_gateway.ino
Flask Server:
- POST /receive-data: giai ma, kiem tra seq, luu DB
- ThreadPoolExecutor(4) ghi DB bat dong bo
- 3 lan thu lai khi SQLite bi khoa
- Luu benchmark: decrypt_ms, seq_ms, log_ms
Database SQLite - 3 bang:
devices | telemetry | benchmark
device_id, last_seq, network_key, lat/lon | device_id, temperature, humidity, pressure, co2... | device_id, decrypt_ms, seq_ms, log_ms, total_ms
Xay dung giai phap truyen tin bao mat giua cac thiet bi IoT

## Slide 16
4.7 Xay dung Dashboard (4 tab)
Tab | Noi dung | Cong nghe
Bieu do cam bien | Gia tri moi nhat + bieu do nhiet do, do ap, CO2, CO, NH3 theo thoi gian | Streamlit + Matplotlib
Ban do Web | Ban do OpenStreetMap voi vi tri cac thiet bi, Mu Cang Chai (21.84, 104.09) | Folium + Leaflet
Du lieu thiet bi | Bang danh sach thiet bi + du lieu telemetry moi nhat + GPS tracking | Pandas DataFrame
Hieu nang | Thong ke benchmark (decrypt/seq/log ms), bieu do 30 request gan nhat | Streamlit charts
Auto-refresh moi 10 giay
Xay dung giai phap truyen tin bao mat giua cac thiet bi IoT

## Slide 17
4.8-4.9 Kich ban va ket qua kiem thu
Ma | Kiem thu | Dau vao | Ket qua
TC01 | Hop le | Key dung, seq moi | DAT
TC02 | Thieu payload | {} | DAT
TC03 | Hex sai | xyz | DAT
TC04 | Sai key | Sai ciphertext | DAT
TC05 | Replay (seq giong) | seq = last_seq | DAT
TC06 | Seq giam | seq < last_seq | DAT
TC07 | Thiet bi khong ro | device_id sai | DAT
TC08 | Nhieu node | Xi_01 + Xi_02 | DAT
TC09 | Mat WiFi | Khong ket noi | DAT
TC10 | Dashboard | Du lieu trong DB | DAT
Ket qua: 10/10 test case DAT

## Slide 18
4.10 Danh gia hieu nang
Chi so | Trung binh | Nho nhat | Lon nhat
AES encrypt (ESP32 HW) | ~17 us | ~16 us | ~20 us
AES decrypt (Python) | ~0.4 ms | ~0.3 ms | ~0.5 ms
Seq check (SQLite) | ~0.3 ms | ~0.2 ms | ~0.5 ms
DB write (SQLite) | ~0.7 ms | ~0.5 ms | ~1.2 ms
Tong xu ly Server | ~1.4 ms | ~1.0 ms | ~2.2 ms
HTTP round-trip (local) | ~80 ms | ~50 ms | ~200 ms
Ket luan:
- Ma hoa < 0.01% thoi gian truyen LoRa (17us vs 725ms)
- nghen la LoRa, khong phai CPU/ma hoa
- Server xu ly ~700 req/s voi 4 thread
Xay dung giai phap truyen tin bao mat giua cac thiet bi IoT

## Slide 19
4.10.5 So sanh AES-128-CBC vs XOR
Kich thuoc | AES (Enc+Dec) | XOR (Enc+Dec) | So sanh
50B | 16.2 us | 10.8 us | XOR nhanh hon
100B | 19.6 us | 20.7 us | Koong bang nhau
200B | 19.1 us | 49.7 us | AES nhanh hon 2.6x
500B | 23.7 us | 95.8 us | AES nhanh hon 4x
1KB | 19.1 us | 222.1 us | AES nhanh hon 11.6x
Ket luan: AES-128-CBC duoc chon: - Do bao mat cao hon XOR - Su dung HW accelerator tren ESP32 (~17us) - Tot hon khi kich thuoc payload lon
Xay dung giai phap truyen tin bao mat giua cac thiet bi IoT

## Slide 20
4.11 So sanh du lieu truoc/sau ma hoa
Truoc ma hoa (Plaintext):
{ "id": "Xi_01", "t": 28.5, "h": 65.2, "p": 1008.0, "co2": 420, "co": 5.1, "nh3": 2.3, "lat": 21.8447, "lon": 105.8426, "seq": 1001 }
Sau ma hoa (Ciphertext hex):
8fa23c91e5a79870b1cd34ef 92ab45c8d0123456789abcde f0123456789abcdef0123456 ...
- Plaintext: ~180 bytes, doc duoc
- Ciphertext: ~208 bytes (IV + ciphertext)
- Hex: ~416 ky tu, khong the doc
- Cung mot plaintext + IV khac nhau = ciphertext khac nhau
Xay dung giai phap truyen tin bao mat giua cac thiet bi IoT

## Slide 21
4.11 Kiem thu tan cong phat lai (Replay Attack)
Kich ban thu nghiem (Hinh 4.16):
Buoc 1: Xi_01 gui payload chua seq=1001
- last_seq (-1) < 1001 -> Chap nhan
- Server luu du lieu, cap nhat last_seq = 1001
- HTTP 200 {'device': 'Xi_01', 'status': 'success'}
Buoc 2: Gui lai NGUYEN payload cu (seq=1001)
- Giai ma thanh cong (ciphertext hop le)
- Kiem tra: 1001 <= last_seq (1001) -> REPLAY!
- HTTP 403 {'reason': 'Replay attack detected (seq <= last_seq)'}
- Khong tao ban ghi telemetry moi
Ket qua: 7/7 test case PASS
Xay dung giai phap truyen tin bao mat giua cac thiet bi IoT

## Slide 22
4.13 Ket qua dat duoc
# | Ket qua
1 | Mo hinh Xi -> Gateway -> Server hoat dong
2 | Mo phong Wokwi ESP32 thanh cong
3 | Bat tay Beacon/ACK 3 buoc
4 | Ma hoa AES-128-CBC tren ESP32 (~17us)
5 | Giai ma AES-128-CBC tren Server
6 | Kiem tra Sequence Number chong replay
7 | Phat hien tan cong phat lai
8 | Luu tru SQLite (3 bang: devices, telemetry, benchmark)
9 | Dashboard Streamlit 4 tab + Ban do Leaflet
10 | 10/10 test case DAT
Xay dung giai phap truyen tin bao mat giua cac thiet bi IoT

## Slide 23
4.12 Han che va huong phat trien
Han che | Anh huong | Huong fix
LoRa chua co phan cung that | Khong co data RSSI/SNR | Thu nghiem voi TTGO T-Beam
Du lieu cam bien mo phong | Khong phai mo truong that | Tich hop BME280, GPS that
Key chung cho moi node | 1 bi mat -> tat bi anh huong | Key rieng moi node + key server
Key hardcode trong firmware | Co the doc duoc | Key provisioning qua efuse
AES-CBC khong co authentication | Co the sua ciphertext | Them HMAC-SHA256
HTTP khong phai HTTPS | Co the ngam truyen | Them SSL certificates
Dashboard khong co auth | Bat ky ai cung xem duoc | Them Streamlit auth
Xay dung giai phap truyen tin bao mat giua cac thiet bi IoT

## Slide 24
KET LUAN
- Xay dung thanh cong he thong truyen tin bao mat IoT
- Ma hoa AES-128-CBC voi HW accelerator (~17us)
- Phat hien tan cong phat lai (replay attack)
- Dashboard truc quan voi ban do Leaflet
- 10/10 test case DAT
Huong phat trien: Thu nghiem voi phan cung that (TTGO T-Beam)
tai Mu Cang Chai, Yen Bai

## Slide 25
CAM ON THAY VA CO
Sinh vien: Do Anh Quan & Ta Huy Hoang